## Slide 1: OVERVIEW
INTERNET CONTROL MESSAGE PROTOCOL
Notes: chapter goals:
understand principles behind network layer services, focusing on data plane:
  network layer service models
  forwarding versus routing
  how a router works
  generalized forwarding
instantiation, implementation in the Internet

## Slide 2: Internet Control Message Protocol (ICMP)
Used by hosts & routers to communicate network-level information
  error reporting
    unreachable host, network, port, protocol
  echo request/reply
    used by ping
  network-layer above IP
    ICMP msgs carried in IP pkts
ICMP message
  ICMP header: 8 bytes
  Start with type and code fields
Type Code Description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 3: Ping Implementations
Sender
  Send ICMP echo with the current timestamp
Destination
  Send ICMP reply (with the original payload in ICMP echo copied)
Sender
  Get the current time
  Get the time carried in ICMP reply
  Difference: one instance of RTT
See more details in PA2 document

## Slide 4: BIT-WISE OPERATIONS IN PYTHON
NETWORK PROGRAMMING
Notes: chapter goals:
understand principles behind network layer services, focusing on data plane:
  network layer service models
  forwarding versus routing
  how a router works
  generalized forwarding
instantiation, implementation in the Internet

## Slide 5: Bit-wise operations on variables
x << y
  returns x with bits shifted to left by y places
    new bits on right-hand-side are zeros
    same as multiplying x by 2y
x >> y
  returns x with bits shifted to right by y places
    same as dividing x by 2y
x & y
  does a bitwise and
    each bit of output is 1 if corresponding bit of x AND of y is 1, otherwise 0
~ x
  returns complement of x
    number you get by switching each 1 for 0 and each 0 for 1
E.g.,
  use to pack ip_version and ip header length into 8 bits
https://wiki.python.org/moin/BitwiseOperators
https://www.tutorialspoint.com/python3/bitwise_operators_example.htm

## Slide 6: Traceroute and ICMP
Source sends series of UDP datagram to destination
  first set has TTL =1
  second set has TTL=2, etc.
  unlikely port number
When nth set arrives to nth router
  router discards and sends source ICMP message (type 11, code 0)
  ICMP message includes name of router & IP address
When ICMP msg arrives
  source records RTTs
Stopping criteria
UDP datagram eventually arrives at dst host
dst returns ICMP “port unreachable” message
source stops
3 probes
3 probes
3 probes

## Slide 7: Traceroute Example Implementations
Send UDP datagram
  Intermediate routers
    respond with ICMP TTL expired
  Final destination
    responds with ICMP “port unreachable” message
Can also use TCP segments (to pass firewalls)
  Approach: similar as UDP
Send segments using ICMP echo
  Intermediate routers
    respond with ICMP TTL expired
  Final destination
    responds with ICMP echo reply